## Slide 1: Analog-to-digital converter (ADC)
Аналогово-цифровой преобразователь (АЦП)
Лекция №6

## Slide 2: ADC introduction
The 12-bit ADC is a successive approximation analog-to-digital converter. It has up to 19 multiplexed channels allowing it to measure signals from 16 external sources, two internal sources, and the V BATchannel.
The A/D conversion of the channels can be performed in single, continuous, scan or discontinuous mode. The result of the ADC is stored into a left- or right-aligned 16-bit data register.
The analog watchdog feature allows the application to detect if the input voltage goes beyond the user-defined, higher or lower thresholds.

## Slide 3: ADC main features
• 12-bit, 10-bit, 8-bit or 6-bit configurable resolution
• Interrupt generation at the end of conversion, end of injected conversion, and in case of
analog watchdog or overrun events
• Single and continuous conversion modes
• Scan mode for automatic conversion of channel 0 to channel ‘n’
• Data alignment with in-built data coherency
• Channel-wise programmable sampling time
• External trigger option with configurable polarity for both regular and injected conversions

## Slide 4: ADC main features
• Discontinuous mode
• Dual/Triple mode (on devices with 2 ADCs or more)
• Configurable DMA data storage in Dual/Triple ADC mode
• Configurable delay between conversions in Dual/Triple interleaved mode
• ADC conversion type (refer to the datasheets)
• ADC supply requirements: 2.4 V to 3.6 V atfull speed and down to 1.8 V at slower speed
• ADC input range: VREF–≤VIN ≤VREF+
• DMA request generation during regular channel conversion

## Slide 6: ADC pins

## Slide 7: ADC clock
The ADC features two clock schemes:
Clock for the analog circuitry: ADCCLK, common to all ADCs
This clock is generated from the APB2 clock divided by a programmable prescaler that allows the ADC to work at f PCLK2/2, /4, /6 or /8. Refer to the datasheets for the maximum value of ADCCLK.
Clock for the digital interface (used for registers read/write access)
This clock is equal to the APB2 clock. The digital interface clock can be enabled/disabled individually for each ADC through the RCC APB2 peripheral clock enable register (RCC_APB2ENR).

## Slide 8: Timing diagram

## Slide 9: Channel selection
There are 16 multiplexed channels
A regular group is composed of up to 16 conversions.
An injected group is composed of up to 4 conversions.

## Slide 11: Temperature sensor, VREFINT and VBAT internal channels
For the STM32F40x and STM32F41x devices, the temperature sensor is internally connected to channel ADC1_IN16.
• Supported temperature range: –40 to 125 °C • Precision: ±1.5 °C
The internal reference voltage VREFINT is connected to ADC1_IN17
The VBAT channel (connected to channel ADC1_IN18) can also be converted as an injected or regular channel.

## Slide 12: Single conversion mode
ADC does one conversion
If a regular channel was converted: – The converted data are stored into the 16-bit ADC_DR register – The EOC (end of conversion) flag is set – An interrupt is generated if the EOCIE bit is set Then the ADC stops.

## Slide 13: Continuous conversion mode
the ADC starts a new conversion as soon as it finishes one
After each conversion: • If a regular group of channels was converted: – The last converted data are stored into the 16-bit ADC_DR register – The EOC (end of conversion) flag is set – An interrupt is generated if the EOCIE bit is set

## Slide 14: Timing diagram

## Slide 15: Analog watchdog
The AWD analog watchdog status bit is set if the analog voltage converted by the ADC is below a lower threshold or above a higher threshold.
An interrupt can be enabled

## Slide 16: Scan mode
ADC scans all the channels selected in the ADC_SQRx registers (for regular channels) or in the ADC_JSQR register (for injected channels)
A single conversion is performed for each channel of the group.
After each end of conversion, the next channel in the group is converted automatically.

## Slide 17
The converted data value from the injected group of channels is decreased by the userdefined offset written in the ADC_JOFRx registers so the result can be a negative value. The SEXT bit represents the extended sign value.
For channels in a regular group, no offset is subtracted so only twelve bits are significant.
Data alignment

## Slide 18: Data alignment

## Slide 19: External trigger and trigger polarity

## Slide 21: ADC interrupts

## Slide 22: Code example RCC_Configuration
void RCC_Configuration_Adc1(void)
{
//for ADC1 on PC0 using IN10
RCC_AHB1PeriphClockCmd(RCC_AHB1Periph_GPIOC, ENABLE);
RCC_APB2PeriphClockCmd(RCC_APB2Periph_ADC1, ENABLE);
}

## Slide 23: Code example GPIO_Configuration
void GPIO_Configuration_Adc1(void)
{
GPIO_InitTypeDef GPIO_InitStructure;
GPIO_StructInit(&GPIO_InitStructure);
//for ADC1 on PC0 using IN10
GPIO_InitStructure.GPIO_Pin = GPIO_Pin_0;
GPIO_InitStructure.GPIO_Mode = GPIO_Mode_AN;
GPIO_InitStructure.GPIO_PuPd = GPIO_PuPd_NOPULL ;
GPIO_Init(GPIOC, &GPIO_InitStructure);
}

## Slide 24: Code example ADC1_Configuration
void ADC1_Configuration(void)
{
ADC_CommonInitTypeDef ADC_CommonInitStructure;
ADC_CommonInitStructure.ADC_Mode = ADC_Mode_Independent;
ADC_CommonInitStructure.ADC_Prescaler = ADC_Prescaler_Div2;
ADC_CommonInitStructure.ADC_DMAAccessMode = ADC_DMAAccessMode_Disabled;
ADC_CommonInitStructure.ADC_TwoSamplingDelay = ADC_TwoSamplingDelay_5Cycles;
ADC_CommonInit(&ADC_CommonInitStructure);

## Slide 25: Code example ADC1_Configuration
ADC_InitTypeDef ADC_InitStructure;
ADC_StructInit(&ADC_InitStructure);
ADC_InitStructure.ADC_Resolution = ADC_Resolution_12b;
ADC_InitStructure.ADC_ScanConvMode = DISABLE;
ADC_InitStructure.ADC_ContinuousConvMode = ENABLE;
ADC_InitStructure.ADC_ExternalTrigConvEdge = ADC_ExternalTrigConvEdge_None;
ADC_InitStructure.ADC_ExternalTrigConv = ADC_ExternalTrigConv_T1_CC1;
ADC_InitStructure.ADC_DataAlign = ADC_DataAlign_Right;
ADC_InitStructure.ADC_NbrOfConversion = 1;

## Slide 26: Code example ADC1_Configuration
ADC_Init(ADC1, &ADC_InitStructure)
ADC_RegularChannelConfig(ADC1, ADC_Channel_10, 1, ADC_SampleTime_480Cycles);
ADC_EOCOnEachRegularChannelCmd(ADC1, ENABLE);
ADC_Cmd(ADC1, ENABLE);
}

## Slide 27
void main(void){
RCC_Configuration_Adc1();
GPIO_Configuration_Adc1();
ADC1_Configuration();
while(1) {
ADC_SoftwareStartConv(ADC1);
while(ADC_GetFlagStatus(ADC1, ADC_FLAG_EOC) == RESET);
ADCResult= ADC_GetConversionValue(ADC1);
}
}