## Slide 1: Digital-to-analog converter (DAC)
Цифро-аналоговый преобразователь (ЦАП)
Лекция №7

## Slide 2: DAC introduction
The DAC module is a 12-bit, voltage output digital-to-analog converter.
The DAC can be configured in 8- or 12-bit mode and may be used in conjunction with the DMA controller.
In 12-bit mode, the data could be left- or right-aligned.
The DAC has two output channels, each with its own converter.
In dual DAC channel mode, conversions could be done independently or simultaneously when both channels are grouped together for synchronous update operations.
An input reference pin, VREF+ (shared with ADC) is available for better resolution.

## Slide 3: DAC main features
Two DAC converters: one output channel each
Left or right data alignment in 12-bit mode
Synchronized update capability
Noise-wave generation
Triangular-wave generation
Dual DAC channel for independent or simultaneous conversions
DMA capability for each channel
DMA underrun error detection
External triggers for conversion
Input voltage reference, VREF+

## Slide 4: DAC channel block diagram

## Slide 5: DAC pins

## Slide 6: DAC output buffer enable
The DAC integrates two output buffers that can be used to reduce the output impedance, and to drive external loads directly without having to add an external operational amplifier

## Slide 8: Timing diagram

## Slide 9: Channel selection
There are 16 multiplexed channels
A regular group is composed of up to 16 conversions.
An injected group is composed of up to 4 conversions.

## Slide 11: Temperature sensor, VREFINT and VBAT internal channels
For the STM32F40x and STM32F41x devices, the temperature sensor is internally connected to channel ADC1_IN16.
• Supported temperature range: –40 to 125 °C • Precision: ±1.5 °C
The internal reference voltage VREFINT is connected to ADC1_IN17
The VBAT channel (connected to channel ADC1_IN18) can also be converted as an injected or regular channel.

## Slide 12: Single conversion mode
ADC does one conversion
If a regular channel was converted: – The converted data are stored into the 16-bit ADC_DR register – The EOC (end of conversion) flag is set – An interrupt is generated if the EOCIE bit is set Then the ADC stops.

## Slide 13: Continuous conversion mode
the ADC starts a new conversion as soon as it finishes one
After each conversion: • If a regular group of channels was converted: – The last converted data are stored into the 16-bit ADC_DR register – The EOC (end of conversion) flag is set – An interrupt is generated if the EOCIE bit is set

## Slide 14: Timing diagram

## Slide 15: Analog watchdog
The AWD analog watchdog status bit is set if the analog voltage converted by the ADC is below a lower threshold or above a higher threshold.
An interrupt can be enabled

## Slide 16: Scan mode
ADC scans all the channels selected in the ADC_SQRx registers (for regular channels) or in the ADC_JSQR register (for injected channels)
A single conversion is performed for each channel of the group.
After each end of conversion, the next channel in the group is converted automatically.

## Slide 17
The converted data value from the injected group of channels is decreased by the userdefined offset written in the ADC_JOFRx registers so the result can be a negative value. The SEXT bit represents the extended sign value.
For channels in a regular group, no offset is subtracted so only twelve bits are significant.
Data alignment

## Slide 18: Data alignment

## Slide 19: External trigger and trigger polarity

## Slide 21: ADC interrupts

## Slide 22: DAC data format
Single DAC channelx, there are three possibilities:
– 8-bit right alignment: the software has to load data into the DAC_DHR8Rx [7:0] bits (stored into the DHRx[11:4] bits)
– 12-bit left alignment: the software has to load data into the DAC_DHR12Lx [15:4] bits (stored into the DHRx[11:0] bits)
– 12-bit right alignment: the software has to load data into the DAC_DHR12Rx [11:0] bits (stored into the DHRx[11:0] bits)

## Slide 23: Code example RCC_Configuration
void RCC_Configuration_Adc1(void)
{
//for ADC1 on PC0 using IN10
RCC_AHB1PeriphClockCmd(RCC_AHB1Periph_GPIOC, ENABLE);
RCC_APB2PeriphClockCmd(RCC_APB2Periph_ADC1, ENABLE);
}

## Slide 24: Code example GPIO_Configuration
void GPIO_Configuration_Adc1(void)
{
GPIO_InitTypeDef GPIO_InitStructure;
GPIO_StructInit(&GPIO_InitStructure);
//for ADC1 on PC0 using IN10
GPIO_InitStructure.GPIO_Pin = GPIO_Pin_0;
GPIO_InitStructure.GPIO_Mode = GPIO_Mode_AN;
GPIO_InitStructure.GPIO_PuPd = GPIO_PuPd_NOPULL ;
GPIO_Init(GPIOC, &GPIO_InitStructure);
}

## Slide 25: Code example ADC1_Configuration
void ADC1_Configuration(void)
{
ADC_CommonInitTypeDef ADC_CommonInitStructure;
ADC_CommonInitStructure.ADC_Mode = ADC_Mode_Independent;
ADC_CommonInitStructure.ADC_Prescaler = ADC_Prescaler_Div2;
ADC_CommonInitStructure.ADC_DMAAccessMode = ADC_DMAAccessMode_Disabled;
ADC_CommonInitStructure.ADC_TwoSamplingDelay = ADC_TwoSamplingDelay_5Cycles;
ADC_CommonInit(&ADC_CommonInitStructure);

## Slide 26: Code example ADC1_Configuration
ADC_InitTypeDef ADC_InitStructure;
ADC_StructInit(&ADC_InitStructure);
ADC_InitStructure.ADC_Resolution = ADC_Resolution_12b;
ADC_InitStructure.ADC_ScanConvMode = DISABLE;
ADC_InitStructure.ADC_ContinuousConvMode = ENABLE;
ADC_InitStructure.ADC_ExternalTrigConvEdge = ADC_ExternalTrigConvEdge_None;
ADC_InitStructure.ADC_ExternalTrigConv = ADC_ExternalTrigConv_T1_CC1;
ADC_InitStructure.ADC_DataAlign = ADC_DataAlign_Right;
ADC_InitStructure.ADC_NbrOfConversion = 1;

## Slide 27: Code example ADC1_Configuration
ADC_Init(ADC1, &ADC_InitStructure)
ADC_RegularChannelConfig(ADC1, ADC_Channel_10, 1, ADC_SampleTime_480Cycles);
ADC_EOCOnEachRegularChannelCmd(ADC1, ENABLE);
ADC_Cmd(ADC1, ENABLE);
}

## Slide 28
void main(void){
RCC_Configuration_Adc1();
GPIO_Configuration_Adc1();
ADC1_Configuration();
while(1) {
ADC_SoftwareStartConv(ADC1);
while(ADC_GetFlagStatus(ADC1, ADC_FLAG_EOC) == RESET);
ADCResult= ADC_GetConversionValue(ADC1);
}
}