## Slide 1: Интерфейсы и протоколы передачи данных UART, RS-232, RS-485, RS-422
Лекция №8

## Slide 2: Виды протоколов передачи данных
симплексные протоколы
полудуплексные протоколы
дуплексные протоколы

## Slide 3: Симплексные протоколы

## Slide 4: Полудуплексные протоколы
RS-485
I2C

## Slide 5: Дуплексные протоколы
RS-232
UART
RS-422

## Slide 6: Виды интерфейсов
Параллельный интерфейс
Последовательный интерфейс

## Slide 7: Виды последовательных интерфейсов
Синхронный интерфейс
Асинхронный интерфейс

## Slide 8: Виды сигналов для передачи данный
небалансный (unbalanced) сигнал (UART, I2C, SPI, RS-232)
балансный (balanced) сигнал (RS-485, RS-422)

## Slide 9: Физический уровень интерфейсов RS-протоколов

## Slide 10: Порядок обмена по интерфейсу RS-232C

## Slide 11: Порядок обмена по интерфейсу UART
Скорость передачи:110, 150, 300, 600, 1200, 2400, 4800, 9600,
19200, 38400, 57600, 115200 бит/с.

## Slide 12: USART main features
Full duplex, asynchronous communications
• Fractional baud rate generator systems
– Common programmable transmit and receive baud rate (refer to the datasheets for the value of the baud rate at the maximum APB frequency.
• Programmable data word length (8 or 9 bits)
• Configurable stop bits - support for 1 or 2 stop bits
• Transmitter clock output for synchronous transmission
Single-wire half-duplex communication
Configurable multibuffer communication using DMA (direct memory access)
Separate enable bits for transmitter and receiver

## Slide 13: USART main features
• Transfer detection flags:
– Receive buffer full
– Transmit buffer empty
– End of transmission flags
• Parity control:
– Transmits parity bit
– Checks parity of received data byte
• Four error detection flags:
– Overrun error
– Noise detection
– Frame error
– Parity error

## Slide 14: USART main features
Ten interrupt sources with flags:
– Transmit data register empty
– Transmission complete
– Receive data register full
– Noise error
– Overrun error
– Idle line received
– Framing error
– CTS changes
– LIN break detection
- Parity error

## Slide 15: USART functional description
The interface is externally connected to another device by three pins (see Figure 296). Any USART bidirectional communication requires a minimum of two pins: Receive Data In (RX) and Transmit Data Out (TX):
RX: Receive Data Input is the serial data input. Oversampling techniques are used for data recovery by discriminating between valid incoming data and noise.
TX: Transmit Data Output. When the transmitter is disabled, the output pin returns to its I/O port configuration. When the transmitter is enabled and nothing is to be transmitted, the TX pin is at high level. In single-wire and smartcard modes, this I/O is used to transmit and receive the data.

## Slide 16: USART functional description
The following pin is required to interface in synchronous mode:
• CK: Transmitter clock output. This pin outputs the transmitter data clock for synchronous transmission corresponding to SPI master mode (no clock pulses on start bit and stop bit, and a software option to send a clock pulse on the last data bit). In parallel data can be received synchronously on RX. This can be used to control peripherals that have shift registers (e.g. LCD drivers). The clock phase and polarity are software programmable. In smartcard mode, CK can provide the clock to the smartcard.
The following pins are required in Hardware flow control mode:
• CTS: Clear To Send blocks the data transmission at the end of the current transfer when high
• RTS: Request to send indicates that the USART is ready to receive a data (when low)

## Slide 17: USART block diagram

## Slide 18: Word length programming

## Slide 19: Word length programming

## Slide 20: Configurable stop bits
• 1 stop bit: This is the default value of number of stop bits.
• 2 Stop bits: This will be supported by normal USART, single-wire and modem modes.
• 0.5 stop bit: To be used when receiving data in Smartcard mode.
• 1.5 stop bits: To be used when transmitting and receiving data in Smartcard mode

## Slide 21: Configurable stop bits
• 1 stop bit: This is the default value of number of stop bits.
• 2 Stop bits: This will be supported by normal USART, single-wire and modem modes.
• 0.5 stop bit: To be used when receiving data in Smartcard mode.
• 1.5 stop bits: To be used when transmitting and receiving data in Smartcard mode

## Slide 22: Single byte communication
The TXE bit is set by hardware and it indicates:
• The data has been moved from TDR to the shift register and the data transmission has started.
• The TDR register is empty.
• The next data can be written in the USART_DR register without overwriting the previous data.
This flag generates an interrupt if the TXEIE bit is set.

## Slide 23: TC/TXE behavior when transmitting
TXE: Transmit data register empty
TC: Transmission complete

## Slide 24: Start bit detection
The sequence is: 1 1 1 0 X 0 X 0 X 0 0 0 0

## Slide 25: Character reception Procedure:
1. Enable the USART
2. Define the word length.
3. Program the number of stop bits in USART_CR2.
4. Select DMA enable (DMAR) in USART_CR3 if multibuffer communication is to takeplace.
5. Select the desired baud rate using the baud rate register USART_BRR
6. Set the RE bit USART_CR1. This enables the receiver which begins searching for a start bit

## Slide 26: Character reception When a character is received:
• The RXNE bit is set. It indicates that the content of the shift register is transferred to the RDR. In other words, data has been received and can be read (as well as its associated error flags).
• An interrupt is generated if the RXNEIE bit is set.
• The error flags can be set if a frame error, noise or an overrun error has been detected during reception.
• In multibuffer, RXNE is set after every byte received and is cleared by the DMA read to the Data Register.
• In single buffer mode, clearing the RXNE bit is performed by a software read to the USART_DR register. The RXNE flag can also be cleared by writing a zero to it. The RXNE bit must be cleared before the end of the reception of the next character to avoid an overrun error.

## Slide 27: Overrun error
An overrun error occurs when a character is received when RXNE has not been reset.
When an overrun error occurs:
• The ORE bit is set.
• The RDR content will not be lost. The previous data is available when a read to USART_DR is performed.
• The shift register will be overwritten. After that point, any data received during overrun is lost.
• An interrupt is generated if either the RXNEIE bit is set or both the EIE and DMAR bits are set.
• The ORE bit is reset by a read to the USART_SR register followed by a USART_DR register read operation.
RXNE: Read data register not empty
ORE: Overrun error
Status register (USART_SR) Data register (USART_DR)

## Slide 28: Selecting the proper oversampling method
select oversampling by 16 (OVER8=0) to increase the tolerance of the receiver to clock deviations.
select oversampling by 8 (OVER8=1) to achieve higher speed (up to fPCLK/8).

## Slide 29: Noise detection from sampled data
• The NF bit is set at the rising edge of the RXNE bit.
• The invalid data is transferred from the Shift register to the USART_DR register.
• No interrupt is generated in case of single byte communication.
The NF bit is reset by a USART_SR register read operation followed by a USART_DR register read operation