## Slide 1: Basic timers
TIM6 and TIM7

## Slide 2: TIM6&TIM7 main features
16-bit auto-reload upcounter
16-bit programmable prescaler used to divide (also “on the fly”) the counter clock frequency by any factor between 1 and 65536
Synchronization circuit to trigger the DAC
Interrupt/DMA generation on the update event: counter overflow

## Slide 3: Basic timer block diagram

## Slide 4: Prescaler description Counter timing diagram with prescaler division change from 1 to 2

## Slide 5: Prescaler description Counter timing diagram with prescaler division change from 1 to 4

## Slide 6: Counting mode: internal clock divided by 1, TIMx_ARR = 0x36

## Slide 7: Counting mode: internal clock divided by 2, TIMx_ARR = 0x36

## Slide 8: Counting mode: internal clock divided by 4, TIMx_ARR = 0x36

## Slide 9: Clock source

## Slide 10: Пример инициализации таймера 7
TIM_TimeBaseInitTypeDef TIM_TBInitStruct;
RCC_APB1PeriphClockCmd(RCC_APB1ENR_TIM7EN,ENABLE);
TIM_TBInitStruct.TIM_Prescaler =8299;
TIM_TBInitStruct.TIM_Period =9;
TIM_TimeBaseInit(TIM7,&TIM_TBInitStruct);

## Slide 11: Функции для инициализации таймеров
void TIM_TimeBaseStructInit (TIM_TimeBaseInitTypeDef * TIM_TimeBaseInitStruct )
void TIM_TimeBaseInit ( TIM_TypeDef * TIMx, TIM_TimeBaseInitTypeDef * TIM_TimeBaseInitStruct )

## Slide 12: Структура для инициализации базовых таймеров TIM_TimeBaseInitTypeDef
uint16_t | TIM_Prescaler
uint16_t | TIM_CounterMode
uint32_t | TIM_Period
uint16_t | TIM_ClockDivision
uint8_t | TIM_RepetitionCounter
TIM_TimeBaseInitTypeDef

## Slide 13: General-purpose timers
TIM9 to TIM14

## Slide 14: TIM2 to TIM5 &TIM9/TIM12 main features
• 16-bit auto-reload upcounter
• 16-bit programmable prescaler used to divide the counter clock frequency by any factor between 1 and 65536 (can be changed “on the fly”)
• Up to 4 independent channels for:
  – Input capture
  – Output compare
  – PWM generation (edge-aligned mode)
  – One-pulse mode output

## Slide 15: TIM9/TIM12 main features
• Synchronization circuit to control the timer with external signals and to interconnect several timers together
• Interrupt generation on the following events:
  – Update: counter overflow, counter initialization (by software or internal trigger)
  – Trigger event (counter start, stop, initialization or count by internal trigger)
  – Input capture
  – Output compare

## Slide 16: General-purpose timer block diagram (TIM10/11/13/14)

## Slide 17: General-purpose timer block diagram (TIM9 and TIM12)

## Slide 18: General-purpose timers (TIM2 to TIM5)

## Slide 19: Clock selection
• Internal clock (CK_INT)
• External clock mode1 (for TIM9 and TIM12): external input pin (TIx)
• Internal trigger inputs (ITRx) (for TIM9 and TIM12): connecting the trigger output from another timer.

## Slide 20: Capture/compare channel 1 main circuit

## Slide 21: Capture/compare channels

## Slide 22: Output stage of capture/compare channel

## Slide 23: Output compare mode, toggle on OC1

## Slide 24: PWM edge-aligned mode Upcounting configuration

## Slide 25: PWM center-aligned mode

## Slide 26: One-pulse mode
• In upcounting: CNT<CCRx≤ ARR (in particular, 0<CCRx), • In downcounting: CNT>CCRx.

## Slide 27: Конфигурация таймера 2
void TIM2_Config(){
TIM_TimeBaseInitTypeDef TIM_TimeBaseStructure;
RCC_APB1PeriphClockCmd(RCC_APB1Periph_TIM2, ENABLE);
TIM_TimeBaseStructure.TIM_Period =8399;
TIM_TimeBaseStructure.TIM_Prescaler = 0;
TIM_TimeBaseStructure.TIM_ClockDivision = 0;
TIM_TimeBaseStructure.TIM_CounterMode = TIM_CounterMode_Up;
TIM_TimeBaseStructure.TIM_RepetitionCounter = 0;
TIM_TimeBaseInit(TIM2, &TIM_TimeBaseStructure);
TIM_ClearITPendingBit(TIM2, TIM_IT_Update);
TIM_ITConfig(TIM2, TIM_IT_Update, ENABLE);
TIM_Cmd(TIM2, ENABLE);
}

## Slide 28
void NVIC_Config(){
NVIC_InitTypeDef NVIC_InitStructure;
NVIC_InitStructure.NVIC_IRQChannel = TIM2_IRQn;
NVIC_InitStructure.NVIC_IRQChannelPreemptionPriority = 0;
NVIC_InitStructure.NVIC_IRQChannelSubPriority = 1;
NVIC_InitStructure.NVIC_IRQChannelCmd = ENABLE;
NVIC_Init(&NVIC_InitStructure);
}

## Slide 29
void TIM2_IRQHandler(void){
if (TIM_GetITStatus(TIM2, TIM_IT_Update) != RESET){
    TIM_ClearITPendingBit(TIM2, TIM_IT_Update);
    PWM_Counter++;
    if(PWM_Counter>=DUTY_0)GPIO_ResetBits(GPIOC,GPIO_Pin_6);
    if(PWM_Counter>=DUTY_1)GPIO_ResetBits(GPIOC,GPIO_Pin_7);
    if(PWM_Counter>=DUTY_2)GPIO_ResetBits(GPIOC,GPIO_Pin_8);
    if(PWM_Counter==199){PWM_Counter=0;GPIO_SetBits(GPIOC,GPIO_Pin_All);}
}
}